- Ploetz, E., S. Laimgruber, S. Berner, W. Zinth, and P. Gilch. “Femtosecond Stimulated Raman Microscopy.” Applied Physics B 87, no. 3 (May 2007): 389–93. https://doi.org/10.1007/s00340-007-2630-x.
  - Lorem ipsum
- Nandakumar, P, A Kovalev, and A Volkmer. “Vibrational Imaging Based on Stimulated Raman Scattering Microscopy.” New Journal of Physics 11, no. 3 (March 25, 2009): 033026. https://doi.org/10.1088/1367-2630/11/3/033026.
  - They didn’t seem that concerned about bandwidth, they just tuned their laser to look at different peaks for different samples. They did fully resolve the spectral dependance of the C-H stretch for one of the beads, but that was to validate that their raman absorption signal matched expected results.
- Tamamitsu, Miu, Yusuke Sakaki, Tasuku Nakamura, G. Krishna Podagatlapalli, Takuro Ideguchi, and Keisuke Goda. “Ultrafast Broadband Fourier-Transform CARS Spectroscopy at 50,000 Spectra/s Enabled by a Scanning Fourier-Domain Delay Line.” Vibrational Spectroscopy 91 (July 2017): 163–69. https://doi.org/10.1016/j.vibspec.2016.07.007.
  - “Frequency-swept laser in SRS spectroscopy is useful for higher-speed CRS imaging applications, achieving 30.8 spectral frames/s with a resolution of 500x480 pixels/frame. However its frequency sweep can only be performed in a frame-by-frame manner, which limits the spectrum acquisition speed, while accessible Raman spectral bandwidth is limited to 300 cm^-1.
  - This one is based off a Ti:S
  - The downside is that the system is a host of moving parts, and a pulse shaper.
  - Furthermore, the “nonlinear increase of the group delay produced by the polygonal Fourier-domain delay line requires a nonlinear sampling of the CARS interferogram.” They have shown that an “analyzable CARS spectrum can still be retrieved by from a constantly digitized waveform by using a theoretically predictable nonlinear resampling approach. While some spectral distortion is expected to occur due to the re-sampling technique, [they] assume it can be reduced by digitizing the analog signal at a higher sampling rate or employing a real-time analog phase-correcting sampling technique.”